/*
HEADER:	CUG149;
TITLE:	6801 Cross-Assembler (Portable);
FILENAME:	A68.DOC;
VERSION:	3.5;
DATE:	08/27/1988;
        update Nov 2011, compiled for lcc-32 windows by HRJ
        update Feb 2019 V3.5+, added S-record by HRJ
        update Aug 2019 V3.5++, added col 1 * comment

DESCRIPTION:	"This program lets you use your computer to assemble
code for the Motorola 6800, 6801, 6802, 6803, 6808,
and 68701 microprocessors. The program is written in
portable C rather than BDS C. All assembler features
are supported except relocation, linkage, and macros.";

KEYWORDS:	Software Development, Assemblers, Cross-Assemblers,
Motorola, MC6800, MC6801;

SEE-ALSO:	CUG113, 6800 Cross-Assembler;

SYSTEM:	CP/M-80, CP/M-86, HP-UX, MSDOS, PCDOS, QNIX;
COMPILERS:	Aztec C86, Aztec CII, CI-C86, Eco-C, Eco-C88, HP-UX,
Lattice C, Microsoft C,	QNIX C;

WARNINGS:	"This program has compiled successfully on 2 UNIX
compilers, 5 MSDOS compilers, and 2 CP/M compilers.
A port to BDS C would be extremely difficult, but see
volume CUG113. A port to Toolworks C is untried."

AUTHORS:	William C. Colley III;
*/

        6800/6801 Cross-Assembler (Portable)

        Version 3.5+

        Copyright (c) 1985 William C. Colley, III

        The manual such as it is.

        Legal Note: This package may be used for any commercial or
        non-commercial purpose. It may be copied and
        distributed freely provided that any fee charged
        by the distributor of the copy does not exceed the
        sum of: 1) the cost of the media the copy is
        written on, 2) any required costs of shipping the
        copy, and 3) a nominal handling fee. Any other
        distribution requires the written permission of
        the author. Also, the author's copyright notices
        shall not be removed from the program source, the
        program object, or the program documentation.

        Note to Users of Previous Versions of the Package

        This version of the 6800/6801 Cross-Assembler package is a
        total rewrite of the old BDS C version. During the recoding, a
        few new "bells and whistles" found their way into the program.
        They are:

        1) Labels can now be as long as an entire line, and all
        characters are significant. In older versions, only 8
        characters were significant.

        2) Listing control has been added to the output routine.
        The listing can be broken up into pages and a running
        header can be added to the top of each page. See the
        TITL and PAGE pseudo-ops for details.

        3) Default extensions for the source, list, and object
        (hex) files are no longer supplied.

        4) Include files are now supported and may be nested.

        Alas, as the sage says, "There ain't no such thing as a free
        lunch." Massive internal changes had to be made to divorce the
        program from the CP/M-80 environment. These changes, the fact
        that full-featured, 8-bit C compilers generate less efficient
        code than BDS C, and the fact that I have leaned on the over-
        powered, slow library function printf() heavily have caused the
        package to run about a factor of 4 slower than the older
        versions. The package also takes 3-6K more disk space to store
        than it used to take.

        On the plus side, however, the code is written in "portable"
        C, so all of the UNIX users, and the new crop of IBM-PC users
        should be able to compile and run the package almost without
        modification. The internal structure of the package is cleaner
        than ever, so it should be very easy to hack on and turn into
        cross-assemblers for other 8-bit processors. Finally, the source
        code has shrivelled almost to nothing since many tasks have been
        off-loaded onto standard library functions, so the need to
        "squeeze" the source code is gone.

        Table of Contents

        1.0 How to Use the Cross-Assembler Package .................. 3
        2.0 Format of Cross-Assembler Source Lines .................. 4
        2.1 Labels ............................................. 5
        2.2 Numeric Constants .................................. 5
        2.3 String Constants ................................... 6
        2.4 Expressions ........................................ 6
        3.0 Machine Opcodes ......................................... 7
        3.1 Opcodes -- No Arguments ............................ 8
        3.2 Opcodes -- One Register Argument ................... 8
        3.3 Opcodes -- One Memory Argument ..................... 8
        3.4 Opcodes -- One Register or Memory Argument ......... 8
        3.5 Opcodes -- One Memory or Immediate Argument ........ 8
        3.6 Opcodes -- Two Arguments ........................... 9
        3.7 Opcodes -- Relative Branches ....................... 9
        3.8 Opcodes -- Direct Addressing ....................... 9
        4.0 Pseudo Opcodes .......................................... 10
        4.1 Pseudo-ops -- CPU .................................. 10
        4.2 Pseudo-ops -- END .................................. 10
        4.3 Pseudo-ops -- EQU .................................. 10
        4.4 Pseudo-ops -- FCB .................................. 11
        4.5 Pseudo-ops -- FCC .................................. 11
        4.6 Pseudo-ops -- FDB .................................. 11
        4.7 Pseudo-ops -- IF, ELSE, ENDI ....................... 11
        4.8 Pseudo-ops -- INCL ................................. 12
        4.9 Pseudo-ops -- ORG .................................. 13
        4.10 Pseudo-ops -- PAGE ................................. 13
        4.11 Pseudo-ops -- RMB .................................. 13
        4.12 Pseudo-ops -- SET .................................. 13
        4.13 Pseudo-ops -- TITL ................................. 14
        5.0 Assembly Errors ......................................... 14
        5.1 Error * -- Illegal or Missing Statement ............ 14
        5.2 Error ( -- Parenthesis Imbalance ................... 15
        5.3 Error " -- Missing Quotation Mark .................. 15
        5.4 Error A -- Illegal Addressing Mode ................. 15
        5.5 Error B -- Branch Target Too Distant ............... 15
        5.6 Error D -- Illegal Digit ........................... 15
        5.7 Error E -- Illegal Expression ...................... 15
        5.8 Error I -- IF-ENDI Imbalance ....................... 16
        5.9 Error L -- Illegal Label ........................... 16
        5.10 Error M -- Multiply Defined Label .................. 16
        5.11 Error O -- Illegal Opcode .......................... 16
        5.12 Error P -- Phasing Error ........................... 16
        5.13 Error R -- Illegal Register ........................ 17
        5.14 Error S -- Illegal Syntax .......................... 17
        5.15 Error T -- Too Many Arguments ...................... 17
        5.16 Error U -- Undefined Label ......................... 17
        5.17 Error V -- Illegal Value ........................... 17

        1

        6.0 Warning Messages ........................................ 17
        6.1 Warning -- Illegal Option Ignored .................. 18
        6.2 Warning -- -l Option Ignored -- No File Name ....... 18
        6.3 Warning -- -o Option Ignored -- No File Name ....... 18
        6.4 Warning -- Extra Source File Ignored ............... 18
        6.5 Warning -- Extra Listing File Ignored .............. 18
        6.6 Warning -- Extra Object File Ignored ............... 18
        7.0 Fatal Error Messages .................................... 18
        7.1 Fatal Error -- No Source File Specified ............ 18
        7.2 Fatal Error -- Source File Did Not Open ............ 18
        7.3 Fatal Error -- Listing File Did Not Open ........... 19
        7.4 Fatal Error -- Object File Did Not Open ............ 19
        7.5 Fatal Error -- Error Reading Source File ........... 19
        7.6 Fatal Error -- Disk or Directory Full .............. 19
        7.7 Fatal Error -- File Stack Overflow ................. 19
        7.8 Fatal Error -- If Stack Overflow ................... 19
        7.9 Fatal Error -- Too Many Symbols .................... 19

        1.0 How to Use the Cross-Assembler Package

        First, the question, "What does a cross-assembler do?" needs
        to be addressed as there is considerable confusion on this point.
        A cross-assembler is just like any other assembler except that it
        runs on some CPU other than the one for which it assembles code.
        For example, this package assembles 6801 source code into 6801
        object code, but it runs on an 8080, a Z-80, an 8088, or whatever
        other CPU you happen to have a C compiler for. The reason that
        cross-assemblers are useful is that you probably already have a
        CPU with memory, disk drives, a text editor, an operating system,
        and all sorts of hard-to-build or expensive facilities on hand.
        A cross-assembler allows you to use these facilites to develop
        code for a 6801.

        This program requires one input file (your 6801 source code) and
        zero to two output files (the listing and the object). The input
        file MUST be specified, or the assembler will bomb on a fatal
        error. The listing and object files are optional. If no listing
        file is specified, no listing is generated, and if no object file
        is specified, no object is generated. If the object file is
        specified, the object is written to this file in "Intel
        hexadecimal" format.

        The command line for the cross-assembler looks like this:

        A68 source_file { -l list_file } { -o/-s object_file }

        where the { } indicates that the specified item is optional. Either
        -o or -s is permitted but not both. -o produces an Intel hex record
        file; -s produces a Motorola hex record file.

        Some examples are in order: file names and extensions are up
        to the user, these are suggested extensions.

        a68 test68.asm source: test68.asm
        listing: none
        object: none

        a68 test68.asm -l test68.prn source: test68.asm
        listing: test68.prn
        object: none

        a68 test68.asm -o test68.hex source: test68.asm
        listing: none
        object: test68.hex

        a68 test68.asm -l test68.prn -s test68.s
        source: test68.asm
        listing: test68.prn
        object: test68.s

        The order in which the source, listing, and object files are
        specified does not matter. Note that no default file name exten-
        sions are supplied by the assembler as this gives rise to porta-
        bility problems.

        2.0 Format of Cross-Assembler Source Lines

        The source file that the cross-assembler processes into a
        listing and an object is an ASCII text file that you can prepare
        with whatever editor you have at hand. The most-significant
        (parity) bit of each character is cleared as the character is
        read from disk by the cross-assembler, so editors that set this
        bit (such as WordStar's document mode) should not bother this
        program. All printing characters, the ASCII TAB character ($09),
        and newline character(s) are processed by the assembler. All
        other characters are passed through to the listing file, but are
        otherwise ignored.

        The source file is divided into lines by newline char-
        acter(s). The internal buffers of the cross-assembler will
        accommodate lines of up to 255 characters which should be more
        than ample for almost any job. If you must use longer lines,
        change the constant MAXLINE in file A68.H and recompile the
        cross-assembler. Otherwise, you will overflow the buffers, and
        the program will mysteriously crash.

        Each source line is made up of three fields: the label
        field, the opcode field, and the argument field. The label field
        is optional, but if it is present, it must begin in column 1. A
        colon at the end of the label is permitted and ignored. The
        opcode field is optional, but if it is present, it must not
        begin in column 1. If both a label and an opcode are present,
        one or more spaces and/or TAB characters must separate the two.
        If the opcode requires arguments, they are placed in the argument
        field which is separated from the opcode field by one or more
        spaces and/or TAB characters.

        Finally, an optional comment can be added to the end of the line
        or replace the entire line. Comments MUST begin with a semicolon, except
        Motorola's column-1 "*" comment format IS supported, Comments can follow
        after the last opcode or operand(s) (with a semicolon). Comments are listed
        but not processed. Thus, the source line looks as below, where the
        { } indicates that the specified item is optional; examples follow.

        {label}{ opcode{ arguments}}{;commentary}

        column 1
        |
        v
        GRONK LDAA X, OFFSET ; This line has everything.
        STAA MAILBOX ; This line has no label.
        BEEP ; This line has no opcode.
        * This line has no label and no opcode.

        ; The previous line has nothing at all.
        END ; This line has no argument.

        4

        2.1 Labels

        A label is any sequence of alphabetic or numeric characters
        starting with an alphabetic. The legal alphabetics are:

        ! & , . : ? [ \ ] ^ _ ` { | } ~ A-Z a-z

        The numeric characters are the digits 0-9. Note that "A" is not
        the same as "a" in a label. This can explain mysterious U
        (undefined label) errors occurring when a label appears to be
        defined. (HRJ note: upper and lower case matters. Also, with
        my revision, labels ending with a ":" have the colon ignored.)

        A label is permitted on any line except a line where the
        opcode is IF, ELSE, or ENDIF. The label is assigned the value of
        the assembly program counter before any of the rest of the line
        is processed except when the opcode is EQU, ORG, or SET.

        Labels can have the same name as opcodes, but they cannot
        have the same name as operators or registers. The reserved
        (operator and register) names are:

        A B AND EQ GE GT
        HIGH LE LT LOW MOD NE
        NOT OR SHL SHR X XOR

        If a label is used in an expression before it is assigned a
        value, the label is said to be "forward-referenced." For
        example:

        L1 EQU L2 + 1 ; L2 is forward-referenced here.
        L2
        L3 EQU L2 + 1 ; L2 is not forward-referenced here.

        2.2 Numeric Constants

        Numeric constants can be formed in two ways: the Intel
        convention or the Motorola convention. The cross-assembler
        supports both.

        An Intel-type numeric constant starts with a numeric
        character (0-9), continues with zero or more digits (0-9, A-F),
        and ends with an optional base designator. The base designators
        are H for hexadecimal, none or D for decimal, O or Q for octal,
        and B for binary. The hex digits a-f are converted to upper case
        by the assembler. Note that an Intel-type numeric constant
        cannot begin with A-F as it would be indistinguishable from a
        label. Thus, all of the following evaluate to 255 (decimal):

        0ffH 255 255D 377O 377Q 11111111B

        A Motorola-type numeric constant starts with a base
        designator and continues with a string of one or more digits.
        The base designators are $ for hexadecimal, none for decimal, @
        for octal, and % for binary. As with Intel-type numeric

        constants, a-f are converted to upper case by the assembler.
        Thus, all of the following evaluate to 255 (decimal):

        $ff 255 @377 %11111111

        If a numeric constant has a value that is too large to fit
        into a 16-bit word, it will be truncated on the left to make it
        fit. Thus, for example, $123456 is truncated to $3456.

        2.3 String Constants

        A string constant is zero or more characters enclosed in
        either single quotes (' ') or double quotes (" "). Single quotes
        only match single quotes, and double quotes only match double
        quotes, as per the examples. Motorola's single-quote for char values
        ('? ) is NOT supported, or is backslash for strings (/hello/).
        In all contexts except the FCC and FDB statements,
        the first character or two of the string constant are all that
        are used. The rest is ignored. Noting that the ASCII codes for
        "A" and "B" are $41 and $42, respectively, will explain the
        following examples:

        "" and '' evaluate to $0000
        "A" and 'A' evaluate to $0041
        "AB" evaluates to $4142

        Note that the null string "" is legal and evaluates to $0000.

        2.4 Expressions

        An expression is made up of labels, numeric constants, and
        string constants glued together with arithmetic operators,
        logical operators, and parentheses in the usual way that
        algebraic expressions are made. Operators have the following
        fairly natural order of precedence:

        Highest anything in parentheses
        unary +, unary -
        *, /, MOD, SHL, SHR
        binary +, binary -
        LT, LE, EQ, GE, GT, NE
        NOT
        AND
        OR, XOR
        Lowest HIGH, LOW

        A few notes about the various operators are in order:

        1) The remainder operator MOD yields the remainder from
        dividing its left operand by its right operand.

        2) The shifting operators SHL and SHR shift their left
        operand to the left or right the number of bits
        specified by their right operand.

        3) The relational operators LT, LE, EQ, GE, GT, and NE can
        also be written as <, <= or =<, =, >= or =>, and <> or
        ><, respectively. They evaluate to $FFFF if the
        statement is true, 0 otherwise.

        4) The logical opeators NOT, AND, OR, and XOR do bitwise
        operations on their operand(s).

        5) HIGH and LOW extract the high or low byte, of an
        expression.

        6) The special symbol * can be used in place of a label or
        constant to represent the value of the program counter
        before any of the current line has been processed.

        Some examples are in order at this point:

        2 + 3 * 4 evaluates to 14
        (2 + 3) * 4 evaluates to 20
        NOT %11110000 XOR %00001010 evaluates to %00000101
        HIGH $1234 SHL 1 evaluates to $0024
        @001 EQ 0 evaluates to 0
        @001 = 2 SHR 1 evaluates to $FFFF

        All arithmetic is unsigned with overflow from the 16-bit
        word ignored. Thus:

        32768 * 2 evaluates to 0

        3.0 Machine Opcodes

        The opcodes of the 6800 and 6801 processors are divided into
        groups below by the type of arguments required in the argument
        field of the source line. Opcodes that are peculiar to the 6801
        are marked with an asterisk. A few notes on the source line
        syntax are in order at this point:

        1) Arguments can be supplied in any order. Thus, for
        example, the following two source lines are equivalent:

        LABEL ADD A X, 0 ;Mumble.
        LABEL ADD A 0, X ;Mumble.

        2) Multiple arguments may be separated from one another by
        spaces, tabs, or commas except that an expression must
        be separated from a following argument by a comma.

        3) In the indexed addressing mode, the expression giving
        the offset may be omitted. The default offset is 0.

        4) The register designators A and B may be appended to the
        opcode itself. Thus, for example, the following two
        source lines are equivalent:

        LABEL CLRA ;Mumble.
        LABEL CLR A ;Mumble.

        3.1 Opcodes -- No Arguments

        The following opcodes allow no arguments at all in their
        argument fields:

        ABA ABX * ASLD * CBA CLC CLI
        CLV DAA DES DEX INS INX
        LSLD * LSRD * MUL * NOP PSHX * PULX *
        RTI RTS SBA SEC SEI SEV
        SWI TAB TAP TBA TPA TSX
        TXS WAI

        3.2 Opcodes -- Register Argument or part-of-opcode:

        The following opcodes EITHER accept one register argument
        A or B (early Motorola syntax); OR the letter A or B is
        part of the opcode (later assembler syntax):

        ADDA	DECA and DECB	PSHA and PSHB
        ANDA and ANDB	INCA and INCB	PULA
        ASLA and ASLB	LDAA and LDAB	SBCA and SBCB
        CLRA and CLRB	LSRA	STAA and STAB
        CMPA and CMPB	ORAA and ORAB	SUBA and SUBB

        3.3 Opcodes -- One Memory Argument

        The opcodes in this group require one argument from the
        following list:

        1) X, expression where expression is 0 thru 255

        2) expression where expression is arbitrary

        The opcodes are:

        JMP JSR STD * STS STX

        3.4 Opcodes -- One Register or Memory Argument

        The opcodes in this group require one argument as per the
        previous group or one of the register specifiers A or B. The
        opcodes are:

        ASL ASR CLR COM DEC INC
        LSL LSR NEG ROL ROR TST

        3.5 Opcodes -- One Memory or Immediate Argument

        The opcodes in this group require one argument from the
        following list:

        1) X, expression where expression is 0-255

        2) #expression where expression is arbitrary

        3) expression where expression is arbitrary

        The opcodes are:

        ADDD * CPX LDD * LDS LDX SUBD *

        3.6 Opcodes -- Two Arguments

        The opcodes in this group require one of the register
        specifiers A or B in addition to an argument from the following
        list:

        1) X, expression where expression is 0-255

        2) #expression where expression is -128 thru 255 (not
        permitted with opcode STA)

        3) expression where expression is arbitrary

        The opcodes are:

        ADC ADD AND BIT CMP EOR
        LDA ORA SBC STA SUB

        3.7 Opcodes -- Relative Branches

        The opcodes in this group require one argument that is an
        expression whose value is in the range *-126 thru *+129. The
        opcodes are:

        BCC BCS BEQ BGE BGT BHI
        BHS BLE BLO BLS BLT BMI
        BNE BPL BRA BRN * BSR BVC
        BVS

        3.8 Opcodes -- Direct Addressing

        Many opcodes of the 6800 and 6801 CPUs allow both one-byte
        direct (or zero-page) addressing and two-byte extended
        addressing. There is no way to explicitly call for one form of
        addressing over the other. The assembler will choose direct
        addressing if ALL of the following conditions are met:

        1) The required expression contains no forward references.

        2) The expression evaluates to 0-255.

        3) The opcode allows direct addressing.

        Otherwise, the assembler will choose extended addressing. Note
        that this makes it desireable to declare your zero-page RAM
        locations at the top of the program so that these locations will
        not generate forward references and foil the assembler's attempts
        to use direct addressing and shrink the object program.

        4.0 Pseudo Opcodes

        Unlike 6800/6801 opcodes, pseudo opcodes (pseudo ops) do not
        represent machine instructions. They are, rather, directives to
        the assembler. These directives require various numbers and
        types of arguments. They will be listed individually below.

        4.1 Pseudo-ops -- CPU

        By default, the assembler does not recognize the additional
        opcodes of the 6801 CPU. This prevents the assembler from
        generating invalid 6800 object code. The additional 6801 opcodes
        are turned on and off by this pseudo-op which requires one
        argument whose value is either 6800 or 6801 (decimal). Thus:

        CPU 6800 ;turns additional opcodes off
        CPU 6801 ;turns additional opcodes on

        4.2 Pseudo-ops -- END

        The END pseudo-op tells the assembler that the source
        program is over. Any further lines of the source file are
        ignored and not passed on to the listing. If an argument is
        added to the END statement, the value of the argument will be
        placed in the execution address line in the hex object
        file. The execution address defaults to the program counter
        value at the point where the END was encountered. Thus, to
        specify that the program starts at label START, the END statement
        would be:

        END START

        If end-of-file is encountered on the source file before an
        END statement is reached, the assembler will add an END statement
        to the listing and flag it with a * (missing statement) error; if
        a hex file is requested, a start-address record will be generated.

        4.3 Pseudo-ops -- EQU

        The EQU pseudo-op is used to assign a specific value to a
        label, thus the label on this line is REQUIRED. Once the value
        is assigned, it cannot be reassigned by writing the label in
        column 1, by another EQU statement, or by a SET statement. Thus,
        for example, the following statement assigns the value 2 to the
        label TWO:

        TWO EQU 1 + 1

        The expression in the argument field must contain no forward
        references.

        4.4 Pseudo-ops -- FCB

        The FCB (Form Constant Bytes) pseudo-op allows arbitrary
        bytes to be spliced into the object code. Its argument is a
        chain of zero or more expressions that evaluate to -128 thru 255
        separated by commas. If a comma occurs with no preceding
        expression, a $00 byte is spliced into the object code. If the
        expression is a string, each char is treated as a byte value. The
        sequence of bytes $FE $FF, $00, $01, $02 could be spliced into
        the code with the following statement:

        FCB -2, -1, , 1, 2

        4.5 Pseudo-ops -- FCC

        The FCC (Form Constant Characters) pseudo-op allows
        character strings to be spliced into the object code. Its
        argument is a chain of zero or more string constants separated by
        blanks, tabs, or commas. If a comma occurs with no preceding
        string constant, an S (syntax) error results. The string
        contants are not truncated to two bytes, but are instead copied
        verbatim into the object code. Null strings result in no bytes
        of code. The message "Kaboom!!" could be spliced into the code
        with the following statement:

        FCC "Kaboom!!" ;This is 8 bytes of code.

        4.6 Pseudo-ops -- FDB

        The FDB (Form Double Bytes) pseudo-op allows 16-bit words to
        be spliced into the object code. Its argument is a chain of zero
        or more expressions separated by commas. If a comma occurs with
        no preceding expression, a word of $0000 is spliced into the
        code. The word is placed into memory high byte in low address,
        low byte in high address as per standard Motorola order. The
        sequence of bytes $FE $FF $00 $00 $01 $02 could be spliced into
        the code with the following statement:

        FDB $FEFF, , $0102

        4.7 Pseudo-ops -- IF, ELSE, ENDI

        These three pseudo-ops allow the assembler to choose whether
        or not to assemble certain blocks of code based on the result of
        an expression. Code that is not assembled is passed through to

        the listing but otherwise ignored by the assembler. The IF
        pseudo-op signals the beginning of a conditionally assembled
        block. It requires one argument that may contain no forward
        references. If the value of the argument is non-zero, the block
        is assembled. Otherwise, the block is ignored. The ENDI pseudo-
        op signals the end of the conditionally assembled block. For
        example:

        IF EXPRESSION ;This whole thing generates
        FCB $01, $02, $03 ; no code whatsoever if
        ENDI ; EXPRESSION is zero.

        The ELSE pseudo-op allows the assembly of either one of two
        blocks, but not both. The following two sequences are
        equivalent:

        IF EXPRESSION
        ... some stuff ...
        ELSE
        ... some more stuff ...
        ENDI

        TEMP_LAB SET EXPRESSION
        IF TEMP_LAB NE 0
        ... some stuff ...
        ENDI
        IF TEMP_LAB EQ 0
        ... some more stuff ...
        ENDI

        The pseudo-ops in this group do NOT permit labels to exist
        on the same line as the status of the label (ignored or not)
        would be ambiguous.

        All IF statements (even those in ignored conditionally
        assembled blocks) must have corresponding ENDI statements and all
        ELSE and ENDI statements must have a corresponding IF statement.

        IF blocks can be nested up to 16 levels deep before the
        assembler dies of a fatal error. This should be adequate for any
        conceivable job, but if you need more, change the constant
        IFDEPTH in file A68.H and recompile the assembler.

        4.8 Pseudo-ops -- INCL

        The INCL pseudo-op is used to splice the contents of another
        file into the current file at assembly time. The name of the
        file to be INCLuded is specified as a normal string constant, so
        the following line would splice the contents of file "const.def"
        into the source code stream:

        INCL "const.def"

        INCLuded files may, in turn, INCLude other files until four
        files are open simultaneously. This limit should be enough for
        any conceivable job, but if you need more, change the constant
        FILES in file A68.H and recompile the assembler.

        4.9 Pseudo-ops -- ORG

        The ORG pseudo-op is used to set the assembly program
        counter to a particular value. The expression that defines this
        value may contain no forward references. The default initial
        value of the assembly program counter is $0000. The following
        statement would change the assembly program counter to $F000:

        ORG $F000

        If a label is present on the same line as an ORG statement,
        it is assigned the new value of the assembly program counter.

        4.10 Pseudo-ops -- PAGE

        The PAGE pseudo-op always causes an immediate page ejection
        in the listing by inserting a form feed ('\f') character before
        the next line. If an argument is specified, the argument
        expression specifies the number of lines per page in the listing.
        Legal values for the expression are any number except 1 and 2. A
        value of 0 turns the listing pagination off. Thus, the following
        statement cause a page ejection and would divide the listing into
        60-line pages:

        PAGE 60

        4.11 Pseudo-ops -- RMB

        The RMB (Reserve Memory Bytes) pseudo-op is used to reserve
        a block of storage for program variables, or whatever. This
        storage is not initialized in any way, so its value at run time
        will usually be random. The argument expression (which may
        contain no forward references) is added to the assembly program
        counter. The following statement would reserve 10 bytes of
        storage called "STORAGE":

        STORAGE RMB 10

        4.12 Pseudo-ops -- SET

        The SET pseudo-op functions like the EQU pseudo-op except
        that the SET statement can reassign the value of a label that has
        already been assigned by another SET statement. Like the EQU
        statement, the argument expression may contain no forward
        references. A label defined by a SET statement cannot be
        redefined by writing it in column 1 or with an EQU statement.
        The following series of statements would set the value of label
        "COUNT" to 1, 2, then 3:

        COUNT SET 1
        COUNT SET 2
        COUNT SET 3

        4.13 Pseudo-ops -- TITL

        The TITL pseudo-op sets the running title for the listing.
        The argument field is required and must be a string constant,
        though the null string ("") is legal. This title is printed
        after every page ejection in the listing, therefore, if page
        ejections have not been forced by the PAGE pseudo-op, the title
        will never be printed. The following statement would print the
        title "Random Bug Generator -- Ver 3.14159" at the top of every
        page of the listing:

        TITL "Random Bug Generator -- Ver 3.14159"

        5.0 Assembly Errors

        When a source line contains an illegal construct, the line
        is flagged in the listing with a single-letter code describing
        the error. The meaning of each code is listed below. In
        addition, a count of the number of lines with errors is kept and
        printed on the C "stderr" device (by default, the console) after
        the END statement is processed. If more than one error occurs in
        a given line, only the first is reported. For example, the
        illegal label "=$#*'(" would generate the following listing line:

        L 0000 FF 00 00 =$#*'( CPX #0

        5.1 Error * -- Illegal or Missing Statement

        This error occurs when either:

        1) the assembler reaches the end of the source file
        without seeing an END statement, or

        2) an END statement is encountered in an INCLude file.

        If you are "sure" that the END statement is present when the
        assembler thinks that it is missing, it probably is in the
        ignored section of an IF block. If the END statement is missing,
        supply it. If the END statement is in an INCLude file, delete
        it.

        5.2 Error ( -- Parenthesis Imbalance

        For every left parenthesis, there must be a right paren-
        thesis. Count them.

        5.3 Error " -- Missing Quotation Mark

        Strings have to begin and end with either " or '. Remember
        that " only matches " while ' only matches '.

        5.4 Error A -- Illegal Addressing Mode

        This error occurs if the index register designator X is used
        with a machine opcode that does not permit indexed addressing or
        if the immediate designator # is used with an opcode that does
        not permit immediate addressing.

        5.5 Error B -- Branch Target Too Distant

        The 6800 relative branch instructions will only reach -126
        to +129 bytes from the first byte of the branch instruction. If
        this error occurs, the source code will have to be rearranged to
        shorten the distance to the branch target address or a long
        branch instruction that will reach anywhere (JMP or JSR) will
        have to be used.

        5.6 Error D -- Illegal Digit

        This error occurs if a digit greater than or equal to the
        base of a numeric constant is found. For example, a 2 in a
        binary number would cause a D error. Especially, watch for 8 or
        9 in an octal number.

        5.7 Error E -- Illegal Expression

        This error occurs because of:

        1) a missing expression where one is required

        2) a unary operator used as a binary operator or vice-
        versa

        3) a missing binary operator

        4) a SHL or SHR count that is not 0 thru 15

        5.8 Error I -- IF-ENDI Imbalance

        For every IF there must be a corresponding ENDI. If this
        error occurs on an ELSE or ENDI statement, the corresponding IF
        is missing. If this error occurs on an END statement, one or
        more ENDI statements are missing.

        5.9 Error L -- Illegal Label

        This error occurs because of:

        1) a non-alphabetic in column 1

        2) a reserved word used as a label

        3) a missing label on an EQU or SET statement

        4) a label on an IF, ELSE, or ENDI statement

        5.10 Error M -- Multiply Defined Label

        This error occurs because of:

        1) a label defined in column 1 or with the EQU statement
        being redefined

        2) a label defined by a SET statement being redefined
        either in column 1 or with the EQU statement

        3) the value of the label changing between assembly passes

        5.11 Error O -- Illegal Opcode

        The opcode field of a source line may contain only a valid
        machine opcode, a valid pseudo-op, or nothing at all. Anything
        else causes this error. Note that the unique 6801 opcodes are
        not valid until they are enabled with the CPU statement.

        5.12 Error P -- Phasing Error

        This error occurs because of:

        1) a forward reference in a CPU, EQU, ORG, RMB, or SET
        statement

        2) a label disappearing between assembly passes

        5.13 Error R -- Illegal Register

        This error occurs either when the register designator A or B
        is used with a machine opcode that does not permit it, or when
        the register designator is missing with a machine opcode that
        requires it.

        5.14 Error S -- Illegal Syntax

        This error means that an argument field is scrambled. Sort
        the mess out and reassemble.

        5.15 Error T -- Too Many Arguments

        This error occurs if there are more items (expressions,
        register designators, etc.) in the argument field than the opcode
        or pseudo-op requires. The assembler ignores the extra items but
        issues this error in case something is really mangled.

        5.16 Error U -- Undefined Label

        This error occurs if a label is referenced in an expression
        but not defined anywhere in the source program. If you are
        "sure" you have defined the label, note that upper and lower case
        letters in labels are different. Defining "LABEL" does not
        define "Label."

        5.17 Error V -- Illegal Value

        This error occurs because:

        1) an index offset is not 0 thru 255, or

        2) an 8-bit immediate value is not -128 thru 255, or

        3) an FCB argument is not -128 thru 255, or

        4) a CPU argument is not 6800 and not 6801, or

        5) an INCL argument refers to a file that does not exist.

        6.0 Warning Messages

        Some errors that occur during the parsing of the cross-
        assembler command line are non-fatal. The cross-assembler flags
        these with a message on the C "stdout" device (by default, the
        console) beginning with the word "Warning." The messages are
        listed below:

        6.1 Warning -- Illegal Option Ignored

        The only options that the cross-assembler knows are -l and
        -o. Any other command line argument beginning with - will draw
        this error.

        6.2 Warning -- -l Option Ignored -- No File Name
        6.3 Warning -- -o Option Ignored -- No File Name

        The -l and -o options require a file name to tell the
        assembler where to put the listing file or object file. If this
        file name is missing, the option is ignored.

        6.4 Warning -- Extra Source File Ignored

        The cross-assembler will only assemble one file at a time,
        so source file names after the first are ignored. To assemble a
        second file, invoke the assembler again. Note that under CP/M-
        80, the old trick of reexecuting a core image will NOT work as
        the initialized data areas are not reinitialized prior to the
        second run.

        6.5 Warning -- Extra Listing File Ignored
        6.6 Warning -- Extra Object File Ignored

        The cross-assembler will only generate one listing and one
        object file per assembly run, so -l and -o options after the
        first are ignored.

        7.0 Fatal Error Messages

        Several errors that occur during the parsing of the cross-
        assembler command line or during the assembly run are fatal. The
        cross-assembler flags these with a message on the C "stdout"
        device (by default, the console) beginning with the words "Fatal
        Error." The messages are explained below:

        7.1 Fatal Error -- No Source File Specified

        This one is self-explanatory. The assembler does not know
        what to assemble.

        7.2 Fatal Error -- Source File Did Not Open

        The assembler could not open the source file. The most
        likely cause is that the source file as specified on the command
        line does not exist. On larger systems, there could also be
        priviledge violations. Rarely, a read error in the disk
        directory could cause this error.

        7.3 Fatal Error -- Listing File Did Not Open
        7.4 Fatal Error -- Object File Did Not Open

        This error indicates either a defective listing or object
        file name or a full disk directory. Correct the file name or
        make more room on the disk.

        7.5 Fatal Error -- Error Reading Source File

        This error generally indicates a read error in the disk data
        space. Use your backup copy of the source file (You do have one,
        don't you?) to recreate the mangled file and reassemble.

        7.6 Fatal Error -- Disk or Directory Full

        This one is self-explanatory. Some more space must be found
        either by deleting files or by using a disk with more room on it.

        7.7 Fatal Error -- File Stack Overflow

        This error occurs if you exceed the INCLude file limit of
        four files open simultaneously. This limit can be increased by
        increasing the constant FILES in file A68.H and recompiling the
        cross-assembler.

        7.8 Fatal Error -- If Stack Overflow

        This error occurs if you exceed the nesting limit of 16 IF
        blocks. This limit can be increased by increasing the constant
        IFDEPTH in file A68.H and recompiling the cross-assembler.

        7.9 Fatal Error -- Too Many Symbols

        Congratulations! You have run out of memory. The space for
        the cross-assembler's symbol table is allocated at run-time using
        the C library function alloc(), so the cross-assembler will use
        all available memory. The only solutions to this problem are to
        lessen the number of labels in the source program, to use a
        larger memory model (MSDOS/PCDOS systems only), or to add more
        memory to your machine.